## Slide 1
March 15, 2019

## Slide 2
GEE file: LandCover/Planet Add QA for Validation Data
Goes through poly1, poly3 and poly5 data to record whether my validation data have good accuracy/high confidence with the help of MODIS EVI timeseries. Also put in cropping intensity.
In the future, these should be done during initial Planet Create Validation Data script
Table:
  Confidence = 0 means no confidence
  Confidence = 1 means MODIS EVI timeseries and reported validation data seem to agree, or at most are 7 days apart
  Confidence or cropping intensity = -1 means no data
Takeaways:
  Noticed that the validation planting date range tends to be late; need to extend plant early to be even earlier (by about a week)
  When it’s really clear when it harvested (i.e. short validation range), the harvest always happens right as the EVI gets to the baseline; harvest doesn’t happen before the baseline or point of max EVI decline
  If there’s a sizeable (i.e. a month) bare soil gap between first and second crop, it’s easier to see p2 and h1; if they come very close together in time, they’re hard to separate in the MODIS timeseries (there’s just a gap of no data between h1 and p2), and it’s easy to get estimates wrong (and therefore will be masked out – source of bias?)
  When there’s a short cycle ‘starter crop’ before the first crop, both the estimates and validation data get confused. Would mask these out and be biased against fields with starter crops in both validation process and in final map.

## Slide 3
Planet imagery workflow
Step | To do | Script/web site
1 | Find locations, years where Planet images are needed. Keep info on shp name, image name(s), and dates downloaded in Image_Lookup file in Google Drive | GEE: LandCover/Planet Image Selection
2 | Download cloud free, high temporal resolution Planet images (may need to pare down on locations, years) | Planet web site. Keep downloaded images in desktop
3 | Upload images as GEE assets | In desktop, keep tabs on asset id, polygon name, etc.
4 | Delineate individual fields, natural veg, agri, urban (houses) and center pivot in Planet imagery, and export as asset into the folder Planet Validation Data. The difference between fields and agri is that the fields contain individual (usu square) fields for timing observation purposes, whereas the agri contains lumped agri for land classification (natural vs agri) purposes. Assets are exported as ‘raw_agri_fc_poly1_year’, etc. need to turn delineated geometries into feature collections in order to export. | GEE: LandCover/Planet manual Field Delineation or Planet OBIA
5 | First import the Planet images and make custom visualizations for each, and map each with its own custom vis. Step through fields in CAR poly and record observed crop timing, export observations as feature collection to asset. Assets are exported as ‘timing_obs_for_polyName_in_year_part#’. Make sure to change the ‘part#’ BEFORE entering obs! 0 for SC, 1 for DC, 3 for TC or DC + failed first crop (2 is other agri in Jake’s classification) | GEE: Planet Create Validation Data v2
5.5 | (for poly1, poly3, and poly5), go back to the timing validation data exported from Planet Create Validation Data v2 and add ‘confidence level’ for my crop timing and crop intensity validation dataset; use MODIS TS to help replace previous crop intensity classification. For confidence labels, use -1 for no data (i.e. no second crop); 0 for no confidence; 1 for confident | GEE: Planet Add QA for Validation Data
6 | Import timing and land cover feature collections. May need to combine timing feature collections into a single fc. Turn feature collection of observations into validation image (might need to first merge multiple obs fcs into a single one), use to do validation. The following are turned into dictionaries of images (or simply images): the observed plant/harvest times; the observed cropping intensity; the observed land cover (agri - 10, center pivot - 20, natural - 30, urban – 40). Use images to do validation of timing and land cover maps. | GEE: Planet Do Validation
Uploading planet images as GEE asset
Properties of each image in PlanetLabs folder
  Year, Month, Day, Satellite
    PS_analytic_4band
    RE_ortho_analytic
    PS_ortho_analytic
    PS_scene_analytic
Asset name is same as the description used in downloading from Planet web site
Lookup table in desktop has Planet order number and description and GEE asset name

## Slide 4
Additional ground reference data for land cover classification

## Slide 5
 | PLOS MT | Soy_pts_agsat_1
Description | Only in Mato Grosso (is the ‘new one’) | Only in Mato Grosso
GEE asset id | users/minghuiz/LandUse/MT_ground_reference_data_PLOS_2017 | users/cloudymccloudface/cohnlab/agroserv/soylc_train_pts_agsat_1
Years | 2005 – 2013 | 2003 - 2017
Property name | clsidYEAR (YEAR = 2005 to 2013) | class
soy-single | 2 | 0
Soy-double | 1 | 1
Agri, nonsoy | n/a | 2
Cotton | 3 | n/a
Pasture/cerrado | 4 | n/a
Soy-cotton | 9 | n/a
Unknown value | 0 | n/a
GEE file LandCover/Soy Classification Trial 2
Reclassify PLOS MT to match soy_pts_agsat_1
Create a single training point for each year instead of lumping multiple years
For the original unknown value, change 0 to -1 and delete that year’s data

## Slide 6
Next

## Slide 7
Crop timing
Clean + mask validation data to create ‘high confidence’ dataset
  Mask out validation data that doesn’t match up with MODIS timeseries
  Mask out validation data based on the width (in days) of the validation range, which is the current proxy for confidence level
  Attach a ‘confidence level tag’ when generating new validation data
Clean + mask crop timing estimates based on crop cycle + peak timing
Attach error distributions to crop timing estimates
  At pixel and field/aggregated scale
  Based on width of validation range and ‘range error’
  Do all pixels/cells have the same error?
  Separate errors for p1, (h1 + p2), and h2 (due to likelihood of clouds impacting TS analysis)
Create SC/DC training and validation data
Delineate fields from Planet images in Matopiba and Mato Grosso
Look at MODIS EVI timeseries over these fields, in addition to Planet images, to determine crop intensity
  Download Planet images over wider area, fewer dates.
  Given the wide range of soy, soy-corn, weed/starter crop-soy-corn timing, it probably doesn’t matter much whether we are sure a crop is soy.
Create field scale SC/DC/TC data
Use as training points for soymap
Create soy vs nonsoy agri training and validation data
Separate MT training points as soy, nonsoy agri (PLOS points have specific nonsoy crops)
Look for spectral, phenological and visual differences among crops
Create training data
Next
New soymaps
Use PLOS training data + previous soy_pts_agsat_1 training data
Center pivot

## Slide 8
For SC vs DC accuracy, normalize by total agri/field, NOT by SC+DC, so the confusion matrix sums to one
For natural vs agri accuracy, try masking edges and masking by crop cycle and peak EVI target only agri
Look at the dates corresponding to the low error fields and see if they represent the full range of crop dates represented by all the fields, because there might be a bias towards fields that were planted at a time when there weren’t clouds. This bias would also be solved if there are many locations of validation data.
Purchase Planet images. Talk to Jen Dawson
Read papers that produce agri datasets. Find one or two that are nice to read and analyze how they write about it.
Use ShareLatex and start outlining
Look at Slack for ‘how to write a paper’ article that Sally shared
Think about the story and figures that illustrate the story

## Slide 9
General problems with land cover classification:
1. Training data are few (especially outside of MT) and perhaps erroneous
  New MT training data from Avery
  Pool existing training data across years
  Create new training data from:
    Planet images
    Google Earth Pro (visual inspection for soy vs nonsoy)
2. Don’t know what characteristics can best separate classes
  Spectrally: Band by band scatterplots to get vegetation index
  Phenologically: Temporal principal components
  Trial and error: Test different input data

## Slide 10
Issue 1: soy vs nonsoy classification is inaccurate
Not enough training data for soy vs non soy in original dataset
There’s a lot of timing variation within soy, perhaps more than for soy vs nonsoy
Solution:
Use new training dataset based in MT (GEE asset ‘MT_ground_reference_data_PLOS_2017’, 675 points from 2003 to 2015)
Train a single classifier across years (to pool up nonsoy agri training points)
Improve the input data by determining what separates soy from nonsoy
  Spectrally: Create band-by-band scatterplots using Sentinel in GEE. Look at multiband indices.
  Phenologically: Temporal principle components applied to individual pixels to find principle trajectories that give the most variation
    See the full variety of soy vs non soy timing. See whether SC/DC soy varies more than soy vs nonsoy
  Use this information to update input data (right now: 8 day aqua composite + 32 day Landsat NDVI + terrain)
Create new soy vs nonsoy training in Matopiba and other areas of Brazil
  Visually: Take the set of existing training points and look in Google Earth Pro for row patterning of soy vs nonsoy to create new training points
  Search for more ground truth data… upcoming survey of soy farms in Brazil
Issue 2: SC soy vs DC soy classification is inaccurate
Sensitive to the set of input training points. Potential reasons:
  Training points aren’t capturing the range of SC vs DC, or are badly geolocated
  Input bands aren’t temporally refined/appropriate
Solution:
Generate training data for crop intensity, especially outside of MT, using Planet imagery. Pay attention to triple cropping/failed first crops – add more nuanced crop intensity classifications. Add in new training dataset (PLOS) for MT. Use these to redo SC/DC classifications.
Temporal principle components: categorize trajectories of SC vs DC to pinpoint what can best separate them in each region
New input bands:
  Peak detection method -> dates of peaks (use dates of certain events, in addition to actual EVI values, as training)
  Sentinel 2 (higher temporal resolution)
Issue 3: center pivot classification
Solution:
Take the difference of the annual min and max EVI, use the difference to find the circle. Then do object based classification of the circle in GEE. Try this with Sentinel for higher revisit time compared to Landsat (get irrigation in recent years)
  Doesn’t solve raster -> vector issue at scale, but could avoid certain densities of center pivot using only the raster layer
Ask Jill Danes at Stanford about center pivot in Brazil

## Slide 11
Next:
Under OBIA script in GEE training, for object based image analysis, see if can automatically get me individual fields
Ask Gabriel if can visually see difference between soy and nonsoy, and list all the potential nonsoy crops options
For center pivot detection, normalize the difference in max and min EVI. Also try to keep the object oriented classification as an image with integers as band values to prevent the raster to vector conversion that’s so hard to scale up
Select new Planet imagery locations in Mato Grosso
  Dense area of soy training points
NEXT Planet image downloads:
For poly6 to 8 (based on soy_pts_agsat1), only download for 2016-2017. these are in MT
Download more matopiba soy polys (poly 2 and 4) for any year
Colab: best way to use Python API with GEE (ipython notebook server)
Do pip install earthengine-api in colab to get virtual machine
Import ee
ee.Initialize()
ee.batch.Task.list() – proves can use earth engine
Docs: github/earthengine-api -> python -> examples -> ipynb -> example stuff