## Slide 1
Method
Prediction of Irrigation Practice in Sparsely Observed Catchments
Minghui Zhang; Sally Thompson, PhD
University of California, Berkeley
Minghui Zhang
University of California, Berkeley
Email: minghuiz@berkeley.edu
Phone: (510) 883 4186
Contact
Botter, G; Porporato, A; Rodriguez-Iturbe, I; Rinaldo, A. “Basin-scale soil moisture dynamics and the probabilistic characterization of carrier hydrologic flows: Slow, leaching-prone components of the hydrologic response”. Water Resources Research, 43, 2007.
Porporato, Amilcare; Daly, Edoardo; and Rodriguez-Iturbe, Ignacio. “Soil water balance and ecosystem response to climate change”. The American Naturalist, 164:5, 2004.
References
Introduction
Discussion
Results
The “predictions in ungauged basins” (PUB) effort has thus far focused on regions with limited human impact.
However, incorporating anthropogenic activity into PUB methods is essential given the high level of development of many basins.
We extended a soil moisture balance and transport model to explore the effects of irrigation on streamflow dynamics (Botter et al, 2007).
Results suggest that different irrigation strategies leave unique fingerprints on a catchment’s streamflow metrics.
Research Questions
How does a given irrigation strategy affect on streamflow for a variety of catchment types?
How heavily does the irrigation strategy influence water supply in each catchment type?
A lumped soil moisture and transfer model (Botter et al. 2007) was modified to account for four possible irrigation sources (Figure 1).
A catchment is described by four soil properties and three climate properties, which are delineated in Figure 1.
Irrigation strategies vary by source and synchronicity. All strategies are assumed to be deficit irrigation with irrigation triggered when soil moisture reaches
Contour plots, etc
Figures 2a,b show the timeseries of streamflow and irrigation was produced for x climate, y soil with deficit irrigation sourced from z source.
The streamflow timeseries for the same catchment with no irrigation (“natural”) is shown for comparison in Figures 2c,d.
A Euclidian distance metric describes the magnitude of change:
timeseries
Conclusions
Next Steps
The distance metric indicates a catchment’s susceptibility to a given irrigation regime. (say how well we can predict irrigation given a type of catchment)
Our results provide a first insight into PUB methodologies that could be employed in heavily managed basins. Application of this work could shed light on worldwide irrigation practices that are unavailable through remote sensing data and serve as a step towards improved water resources planning in basins affected by human activity.
To expand on our first research question, we will vary the irrigation regime. We will include fixed scheduling of irrigation and an ET balance irrigation method.
To address our second research question, we will use statistical techniques to compute the likelihood of each irrigation practice in a set of potential irrigation scenarios using streamflow data alone.
Our predictions in irrigation will be validated through comparison with basins for which irrigation and streamflow details are already known.
Each catchment type can be described by its position along two axes (Porporato et al., 2004):
An environmental and social impact metric was used to sum up the impact of each irrigation technique on:
GW storage
SA storage
Irrigation needs not met
Average streamflow with irrigation compared to average streamflow in natural conditions
Add each parameter definition in the diagram
Enviro impact metric plot
Mention sync and no sync?