## Slide 2
TO DO
General climate classification
relook at climate classification.R and incorporate Xue’s indeces in classification; compare climate classification.R’s classifications into snow/no snow and seasonally dry/not seasonally dry with what Xue’s indeces would do
Code up Schaefli’s snow dominated catchments (requires hypsographic curve and z* calibration…)
Lit review of how pdfs are treated in seasonal climates beyond Marc’s work. Can any other method be applied to ours?
Marc’s seasonally dry stuff
Find a and b recession constants instead of guessing
Check whether pdf(qds) match up in NSE calculations.
Check the Testing Marc Seasonally Dry.R code for holes
In general, NSE is very sensitive, perhaps due to fast variation in pdf value at lower qd values. Consider how positioning of points, rather than a real change in pdf agreement, will impact NSE.
Use numeric pdf for dry season going forward; if have time, do these less important things:
  figure out why analytic1 performance changes with number of breaks in histogram
  re-derive analytic2 equation, which is completely off

## Slide 3
(Schaefli et al., 2013)
Snow-dominated pdfs for “zone I and II catchments” – i.e. they are affected by multiday snow storage, but the snow melts within a season (no glaciers)
Need two new parameters to build on original Botter:
A*: this is found using A*= A * P(Z > z*). The P(Z > z*) means portion of basin that is above a threshold altitude z*, and this P value can be found using the hypsographic curve (which shows the portion of land that exists at various elevations in a basin). To determine z*, the method uses calibration. Once all other parameters are found, adjust z* to fit the observed pdf. NEED TO RETURN TO THIS because need to find hypsographic curve using ArcGIS? Also, what is the use of having to calibrate z* in ungauged basins? Can there be another way to find z*, like relations between elevation and temperature?
kD: this is from tau_D, which is the mean duration of periods with temperatures less than 0 Celsius
The regular (summer) recession will be k, and they calculated it using Brutsaert-Nieber 1977, using Q below 90% of the summer flow quantile.
Did they find precip statistics from the responsive area only or for the whole area?